## Slide 1: The Cascina activity on squeezing
Jean-Pierre Zendri
On behalf of the squeezing team

## Slide 2
Squeezing activity in Cascina
Aim: Construction of a vacuum squeezer following the AdV squeezing TDR design. Details in VIR-0411A-152
Homemade SHG
Linear single resonant OPO
EGO support
  Logistical and services (clean room, racks, computers, network,..)
  Specific tasks (in vacuum faraday isolator, DC photodiodes, DC power supply, cabling, PZT HV drivers, resonant EOM…)
  Discussion and expertise in many fields.
Goal: 12 dB of squeezing in the audio frequency band
The main financial support is from INFN (Ge, Na, RomeI, RomeII, Pi, Pd/Tn) plus in kind support from other Virgo-Labs.
The construction began in the 1500W clean room in September 2015.

## Slide 3
The 1500W optical layout
Green Line SHG+MZ+MC532
Homodyne line MC1064+ homodyne
SHG Cavity
Mach Zhender
MC532
MC1064
Homodyne
OPO Line OPO cavity
Other OPLL, electronics
OPO
cavity

## Slide 4
Second Harmonic Generation (SHG)
Crystal: PPKTP 9.3×1.2×1 mm
Phase matching
Double pass conversion
Best efficiency @ 305 Kelvin
Double pass efficiency <1%
HR coating
ROC 8 mm
AR coating
1064&532
n=1.8306
9.3 mm
PPKTP
Virgo Week Cascina May 4th, 2016

## Slide 5
Cavity enhanced SHG
Cavity design and mode matching
Achieved Mode matching
Cavity controls
ADC
DAC
Real time Processing
Error signal
HV PZT driver or Peltier
NI PXI
Temperature stability 1 mK rms (24 bit 100 Hz)
PDH (14 bit 20 kHz)
M. Leonardi

## Slide 6
Installed SHG efficiency
The present incoupling mirror reflectivity is 92% (tested also 96%).
Long term green power stability
SHG goal (Pgreen >100 mW) achieved
At the optimal crystal temperature of 305 Kelvin
Convertion efficiency order of 95%
Up to 200 mW produced
M. Leonardi
Order of few % due to the pump laser fluctuations
Too much!! Need of stabilization of the pump

## Slide 7
Green Power Stabilizazion: Mach-Zhender
Mach Zehnder goal achieved
Unbalanced MZ
Beam splitter transmittivity
Tp :10%
Ts :1%
PZT
Green Power at the MZ output
Required a stability of at least 1%

## Slide 8
The green Mode Cleaner MC532
The green line is almost completed. SHG Ok, MZ Ok, MC532 integration this week
Triangular cavity:
Finesse 600
FSR 514 MHz
Optical path length 582 mm
Invar
The assembled MC532 is ready
the integration in the squeezer optical bench is currently under way
99.5%
99.5%
99.98%
271 mm

## Slide 9
Homodyne: The IR mode cleaner
Triangular cavity:
p finesse 3000
s finesse 250
Optical lenght 582 mm
Invar
Cavity transfer function: A/B
Installed and locked. OK
white
noise
A
B

## Slide 10
SAT ADC/DAC tested on MC1064
The commercial NI PXI has been recently substituted with the new SAT ADC/DAC (24 bit 320 kHz).
PDH with autolocking implemented
Example:
Error signal
PDH Open loop gain

## Slide 11
Homodyne detection
Audio frequency:
For the differential channel it is required a noise floor 15-20 dB below the shot noise limit @ Local Oscillator 1 mW
Above 200 Hz achieved the homodyne audio frequency goal
Self substraction scheme
Nominal photodiodes quantum efficiency >99%
Low noise amplifiers AD8625
Below 200 Hz noise dominated by acoustic and air flow noise

## Slide 12
Homodyne detection
Common Mode Rejection :
Radio frequency:
  The homodyne rf line at 7 MHz still have to be tested
  7MHz is the planned Coherent control loop frequency
Ok
Homodyne line installed: Audio line Ok, rf line to be tested
Best achieved (in the kHz region) about 80 dB
Pump
Mod.
l/2

## Slide 13
The OPO cavity
The OPO is presently the only subsystem that will incorporate superpolished optics.
The superpolished and coated (LMA) crystals and the incoupling mirrors has been delivered few weeks ago.
All the components are ready for the cavity assembly.
LC
HR coating
ROC 12 mm
92% @1064
20% @532
9.2 mm
PPKTP

## Slide 14
Optical Phase Locked Loop (OPLL)
Main laser | Slave laser | RF Offest | 
AdV main laser | Squeezer main laser | TBD | Locking the squeezer to AdV
Squeez main las. | Aux laser 1 | 20 MHz | OPO length control
Squeez main las. | Aux laser 2 | 7 MHz | Coherent control
3 OPPL required
Residual Phase jitter must be kept below 20 mrad rms
PLL
Slow: Peltier
Fast: PZT
nbeat
nref

## Slide 15
OPLL-PCB
I/O serial protocol
ADC/DAC manage
Diagnostics
Autolocking
Bandwidth limits (laser PZT resonances)
Measured
for Mephisto 500NE
100 kHz unitary bandwidth can be approached using notch filters

## Slide 16
OPLL-results
Optical Phase Locked Loops between Mephisto 500 NE and lightwave
Residual phase jitter 15 mrad (unitary bandwidth 45 kHz)
Long term operation
LONG term operation
PLL electronics ready for installation

## Slide 17
Direct Digital Synthetizer (DDS)
Needed at least 12 low noise rf channels 5÷100 MHz
4 locked rf channels each channel has remotely selectable
amplitude (max 7 dBm)
frequency (up to 500 MHz)
phase
AD9910: 14 bit 1 GSPS
USB or Ethernet
Linux embedded module
External Clock: Wenzel crystal @ 500 MHz

## Slide 18
Direct Digital Synthetizer (DDS) results
Absolute phase noise
Relative phase noise
Spectrum analyser
FFT analyzer
SR540
LP
ChI
ChJ
ChI
Well within our requirements

## Slide 19
Summary
Homodyne Line | 
MC1064 | Installed
Homodyne | Installed
OPO line | 
OPO | close to be assembl.
Green Line | 
SHG | Installed
MZ | Installed
MC532 | Instal. underway
OPL and electronic | 
OPLL PCB | Ready
DCC | Ready
Main Controls | Work in progress
Status of squeezer:

## Slide 20
Short term activity
Squeezer commissioning
Conclude the squeezer assembly
Draw build and install the beam dumps and absorbers
House the optical bench and the homodyne detector in a dedicated box
Choerent Control
Hardware and software improvement, cabling
Add more superpolished components

## Slide 21
Logbook
More details in
http://slwebtest.virgo.infn.it/osl_squeezing/