## Slide 1
Matthieu Gosselin
5W fibered electro-optic phase modulator
GraWIToN
GW Initial Training Network
November, 17th 2015, EGO
Virgo Week

## Slide 2: Summary
GraWIToN
GW Initial Training Network
GraWIToN project
Phd overview
First developments and results

## Slide 3: Summary
GraWIToN
GW Initial Training Network
GraWIToN project
Phd overview
First developments and results

## Slide 4: GraWIToN Training Project
GraWIToN
GW Initial Training Network
  High power optical components
  Materials (Silicon Carbide, Adhesive-Free Bond...)
  Computer simulations
  Data Analysis
14 PhD students in public and private institutions
Funded by European Commission under FP7-Marie Curie Actions

## Slide 5: GraWIToN in the Virgo Collaboration
GraWIToN
GW Initial Training Network
Data Analysis
Simulation
New technologies
Rudy Nahed, Boostec Tarbes, Silicon carbide for stray light control (June 15, Oct 15, 2016)
Jose M. González Castro, University of Pisa, Computer intensive simulation of optical systems and components (regular basis)
Gang Wang, INFN (Pisa), Multi Band Template Analysis, multimessenger (regular basis)
Shubhanshu Tiwari, INFN (Trento), cWB : Bursts Analysis (regular basis)
Daniel Töyrä, University of Birmingham, Computational modeling of advanced laser-interferometric gravitational wave detectors (2 months in 2016)
Marina Trad Nery, AEI Hannover, Power stabilization at and below the shot noise limit (Oct 15, 2016)
Omar De Varona, LZH Hannover, Dynamics of high power fibre amplifiers (2016)

## Slide 6: Summary
GraWIToN
GW Initial Training Network
GraWIToN project
Phd overview
First developments and results

## Slide 7: Details on my Phd position
GraWIToN
GW Initial Training Network
Input optics components for the upgrade of the 2nd and 3rd generations of gravitational waves detector
    1st year : fibered Electro-Optic Modulator for ≤10W
  2nd year : fibered Electro-Optic Modulator for ≥ 100W
  3rd year : fibered Faraday isolator for ≥ 100W
Gain experience with EOM before working on Faraday Isolator
Increasing power step by step
November 2014 - November 2017

## Slide 8: Injection into vacuum with a fiber
GraWIToN
GW Initial Training Network
Fibered the transmissions before Mode cleaner
Reduction of the noises
Ease the transmission on the in-vacuum bench
Fibered EOM
Fibered FI
and Power Control
Possible futur design

## Slide 9: Fibering expectations
GraWIToN
GW Initial Training Network
Noises, free space to vacuum injection
Better control on the propagation
No alignment issues, beam jitter
Fiber can be directly brought inside the tower
Noises due to the free space propagation
Fibering will induced other noises that have to be characterized
Phase noise induced by the fiber can be canceled with a retroaction loop on the EOM or other “phase” actuators
Already improved by covering the beam path
Could be improved by fibering everything

## Slide 10
EGO optics group (Eric Genin, Gabriel Pillant) : experience in high power electro-optics components
LZH (3 month secondment) : Abilities in high power injection into fibers, Use of a single frequency high power laser inducing non linear effects
Boostec (1 month secondment) : use of silicon carbide as beam dumps in our application
GraWIToN
GW Initial Training Network
Trainings and Experiences
Good overview of all the fields of GW detection
Meet many actors of the project
GraWIToN school : Useful lectures on high power optical components

## Slide 11: Summary
GraWIToN
GW Initial Training Network
GraWIToN project
Phd overview
First developments and results

## Slide 12: Non linear effects
GraWIToN
GW Initial Training Network
Raman, Four waves mixing, Brillouin…
Field of a single frequency laser
Intensity of the light
Electrostriction , Bragg Mirror
Incident light is back reflected
Increase with
Power
Length
Narrowband

## Slide 13: Brillouin effect into fibers
GraWIToN
GW Initial Training Network
200W CW single frequency in a 15μm silica core
Few centimeters of propagation
Behavior for microstructured fiber not well defined by the theory
It has been used for powers to up 30W in the AEI at Hannover
LMA-PM-15
Upcoming tests on new fibers
LMA-PM with larger core : 25μm , 30μm
Hollow core fibers : propagation into air
Power densities divided by 4
No non-linear effects anymore
Compromise between beam quality and propagation
5 meters no brillouin effect

## Slide 14: Injection into fibers-Connectors
GraWIToN
GW Initial Training Network
Losses Noises… ALphanov
Current connectors
High power SMA-905
Temperature elevation ~7°C/W
10W misaligned
Strip out the mismatched light
New generation of connectors
end facet
melted
Laser micromachined Higher power tolerance

## Slide 15: EOM set-up
GraWIToN
GW Initial Training Network
High power Laser
coupling
EOM
Plastic box
Free space injection Or Fibered laser
Plastic box to confine the component as much as possible from outside perturbations
Breadboard to be easily move from a place to another, from a laser to another, keeping the alignment
Breadboard

## Slide 16: Electro-optic modulator
GraWIToN
GW Initial Training Network
Electrodes
Crystals
Peltier
Control the temperature with peltier modules to reduce the noises (in particular RAM)
5W electro-optic modulator with 4 modulation frequencies
Design with the mechanics and electronics department of EGO

## Slide 17: Characterization Set-up
Mach-Zehnder interferometer
Electronics layer
Injection part
Beating between the incident light and the modulated light
87% coupling through the all fibered EOM
Mixing with the reference signal Study the characteristics of the sidebands
ω0
ω0-ωm
ω0+ωm
ωm
17

## Slide 18
Output power
Error Signal
Apply correction
Slow shift of the arms
Lock Mach-Zender
Lock of the Mach-Zehnder interferometer in order to cancel its phase noise
Upcoming measurements : full characterization
Dark fringe
Bright fringe
GraWIToN
GW Initial Training Network
Residual Amplitude Modulation
EOM phase noise
Vπ, modulation depth
18

## Slide 19: Conclusion
GraWIToN
GW Initial Training Network
Increase the power : up to 200W at EGO
New fibers for higher power : larger core, hollow core in order to avoid non linear effects
Control of the characteristics with feedback loops
Up to 200W single frequency in Hannover (early 2016)
Further developments
Functional 5W electro-optic modulator under characterization
19

## Slide 20
Thank you for your attention
GraWIToN
GW Initial Training Network
Matthieu Gosselin, gosselin@ego-gw.it