## Slide 1: Length sensing simulation: effect of an offset on MICH
Jean-francois Hayau, Francois Bondu

## Slide 2: Outline
Length sensing on ASY_DC
Offset on MICH instead of offset DARM?
Conclusion

## Slide 3
0ptickle model (NDRC) :
Transfer function on ASY_DC:
Length sensing on ASY_DC
Arm cavity length 2999,9m LSRC 31,427m LPRC 30,099m Schnupp asymmetry 0.03m | Fmod1 6270659 Hz Fmod2 56435931 Hz Fmod3 8360879 Hz Offset DARM 1.10-11m
Transfer function of DARM to ASY_DC decrease at low frequencies due to radiation pressure effect.
=> Difficulties to extract DARM signal from noise signals.

## Slide 4
Interest of an Offset on MICH : radiation pressure effect could be reduced.
Transfer function on ASY_DC in a simple configuration: Interferometer without recycling cavities
=> with offset MICH effect of radiation pressure is not observed .
Offset on MICH instead of offset DARM?
Offset DARM = 1.10-11m
(No Offset DARM ) Comparable sensitivity with
Offset MICH = 2Fcav/π .Offset MICH= 5,7.10-9m

## Slide 5
Test in a configuration with a Power recycling cavity ( no SRCL, MSRC configuration)
Offset on MICH instead of offset DARM?
Offset DARM = 1.10-11m
(No Offset DARM ) Comparable sensitivity with
Offset MICH = 2Fcav/π .Offset MICH = 5,7.10-9m

## Slide 6
Test in a configuration with a Power Recycling Cavity and Signal Recycling cavity (MSRC configuration)
=> SRC leads to radiation pressure effect also is the case of an offset on MICH
Offset on MICH instead of offset DARM?
Offset DARM = 1.10-11m
(No Offset DARM ) Comparable sensitivity with
Offset MICH = 2Fcav/π .Offset MICH = 5,7.10-9m

## Slide 7
Length sensing on ASY_DC is disturbed by radiation pressure effect.
Comparison of an offset on DARM and on MICH shows an interesting way to reduce radiation pressure effect:
  For commissioning , configuration with an offset on MICH without SRC avoid radiation pressure effect,
  Signal recycling cavity leads to radiation pressure effect.
Conclusion