## Slide 1: New DSP Installation Notes
A. Gennai, D. Passuello, G. Ballardin (EGO)

## Slide 2: Purpose
Purpose of this presentation is clarify few basic points about new DSP installation:
  What we need
  What we can/cannot do
  What will change for users

## Slide 3: What we need
Why new DSP
  Motivations are quite obvious and have been presented several times
    Old DSP have been running continuously for more than 10 years.
    Monolithic Payloads will require additional computational power
      Dynamics: need to implement LowNoise 1&2 at mirror level and LowNoise at marionette level.
      Improve robustness

## Slide 4: What we can/cannot do
We will replace at the same time both DSPs involved in suspension control
  Replacement of a single DSP would require using two different DSP servers running simultaneously and two different custom versions of Damping (to be developed only for this specific purpose).
We will use only TOLM
  Even if new DSP can handle DOL and TOLM, using both would require a custom Damping version.
  New DSP and old DSP could anyway communicate using a TOLM/DOL gateway as the one already in use.
Two DSPs hosted in the same crate will talk each other using a serial link (115.2kbit/sec with old DSP, 50 Mbyte/sec with new one)

## Slide 5: What will change for users
Compiler and DSP Server are new but Damping will not change.
  DSP Server accepts the same CM commands as before
  Damping user interface was not changed
  DSP code doesn’t need to be changed: just load code (the so called ‘card’), compile and download
  During transition phase we will have some old and some new DSPs. Some minor trouble is expected in handling different configurations

## Slide 6: What will change in other VIRGO subsystems
DAQ + GC
  (Replacement of DOL with TOLM)
Galaxy will use TOLM instead of VME bus for Camera/PSD data
  Greatly improved reliability (DSP side)

## Slide 7: What was/wasn’t tested
Today we have 26 DSP boards available (21 needed)
Control loops on both upper and lower DSP where successfully tested last spring (with DOL)
DAQ and basic GC communication was tested in the VTF
Already implemented but still to be tested is the Galaxy communication via TOLM

## Slide 8: Installation Sequence
Installation planning is out of the scope of this presentation, nevertheless …
Preferred installation sequence is the following:
  PR  BS  OB
  IB+MC+BC  NI+NE  WI+WE
Two shifts per suspension (or couple of suspensions) should be enough for both DSP and DAQ/GC sides.