## Slide 1: ENV training Outline
Introduction – Environmental noise hunting, WHAT IS IT?
Part I – Sensors and channels (Irene)
Part II – Experimental techniques (Federico)
Part III – Data analysis techniques (Irene)

## Slide 2: ENV training session Part I Sensors and Channels
Irene Fiori on behalf of the ENV team
VIR-0947A-19
Virgo training sessions
September 26 2019

## Slide 3: Outline of Part I
Introduction: what is ENV noise disturbing Virgo?
Environmental sensors
  Type
  Location
  What they measure
Channels
  Names
  Where to find the data

## Slide 4: Introduction
Environmental noise hunting, WHAT IS IT?

## Slide 5: Environmental influences on GW interferometer
Radio waves
(6MHz, 8MHz, 56MHz)
Excite mechanical modes of mirrors and optical benches suspensions
Excite vibrations of vacuum pipes and tanks, optics on in air benches
Imprint phase noise on spurious scattered light beams
Seism & Sounds
Slow ground motion
Electro Magnetic fields
Act on mirror MAGNETS
RF modulated laser beam
used for angular and longitudinal controls

## Slide 6: Self-inflicted noise
Chillers
Vacuum pumps
Air ventilation
Electrical system, cables
Illumination, Uninterruptible Power Supply
Electronic devices,
cooling fans

## Slide 7: Distant but loud ….
7

## Slide 8: Part I
Sensors and channels

## Slide 9
WEST arm
3km
NORTH arm
3km
CEB
NEB (WEB)
MCB

## Slide 10: ENV probes
CEB
MCB and NEB (WEB)

## Slide 11: Building monitors
SOIL VIBRATIONS
Microphone
Infra sound
0.1 – 10kHz
GURALP velocimeter
0.1Hz to 100Hz
Also _NEB, _WEB, _MCB
SEA
WIND
ANTHROPIC
Site infrastructure

## Slide 12: Building monitors
MAGNETOMETERS
Magnetometers
0.1-10kHz
_NEB, _WEB, _MCB
SIDEBANDS

## Slide 13: Building monitors
Microphone
Temperature probes
Temperature
1Hz sampling
RF antenna:
signal is demodulated around Virgo’s
Laser modulation frequencies: 6MHz, 8MHz, 56MHz
20kHz sampling
Microphone
Infra sound
0.1 – 10kHz
Air conditioners OFF
Mostly RACKS cooling fans

## Slide 15
3 PHASES of MAINS
Voltage monitors
Current monitors
Building monitors

## Slide 16: ENV probes
v
IN-AIR
BENCH
Acoustically isolated area
suspended to GAS filter
SUSPENDED IN_VACUUM
BENCH
CEB
MCB and NEB (WEB)
= Electronic racks

## Slide 17: Monitor of in-air benches
1 Microphone
1 Accelerometer (high frequency)
1 Tri-axial accelerometer (low frequency)
1 Temperature +Humidity sensor attached to bench
1 Temperature + Humidity + Pressure in the Clean Room
1Hz-500Hz
10Hz-2kHz
Also:
LB,EIB,SQZ,TCS_CO2_NI
TCS_CO2_WI, EMCB
Peaks 10-40Hz are bench modes

## Slide 18: ENV probes
Vacuum chambers
Cryogenic vacuum traps
CEB
MCB and NEB (WEB)
View-ports

## Slide 19: Monitor of critical spots
Possible sources of back-scattering:
Optical windows
Beam dumps
Cryogenic traps
TOT of 36 accelerometers
inner tank
outer tank

## Slide 20: AUXILIARY slow monitors
Monitors of infrastructure 1 Hz sampling
(V1:INF_* V1:HVAC_* V1:VAC_*)
Air&Water Temperature&Pressure
Power consumption of big switching loads (chillers, heaters)
Illumination (*LUX*)
Air conditioners Hot&Cold loops
Vacuum valves, LN2 levels, residual gas pressure, …

## Slide 21
Weather station and Lightning detector
External magnetometers
External monitors

## Slide 22
External monitors

## Slide 23: Environmental probes DOCUMENTATION
MAPS:
  HARDWARE inventory MAP http://slwebtest.virgo.infn.it/ifoapp/
  • ENV_maps_24_07_2018.pdf (with location of FAST and SLOW probes)
  • Map_ENV_sensors_cirone.pdf (with location of FAST probes, and associated NAMES)
  INF sensors interactive MAP https://scientists.virgo-gw.eu/IMMS/
SENSORS specs:
  https://scientists.virgo-gw.eu/EnvMon/sensorDocs.htm
HARDWARE inventory
(active directory account)
FAST sensors with Channel names
(pdf file)
IFN sensors interactive map

## Slide 24: Channel name conventions
V1:ENV_LOCATION(_SUBLOCATION)_SENSOR(_DIRECTION)
CEB = Central Building
(NEB,WEB,MCB)
LLR = Laser Lab Room
….
BS = Beam Splitter
….
EIB = External Injection Bench
….
SEIS
ACC
MAG
MIC
VOLT
CURR
TE
HU
PRES
RF
….
Orthogonal triplets:
X,Y,Z  Z is along beam direction, Y is vertical
N,W,V  N= along N arm, W=W arm, V= vertical
CT = CryoTrap
CHILLER
HEATER
LINK = link pipe
….
For a more complete description
CHANNEL DATABASE
http://slwebtest.virgo.infn.it/ifoapp/
Z is along beam
Channel naming conventions
VIR-0223B-14
https://tds.virgo-gw.eu/ql/?c=10250

## Slide 25: DATA streams: OFFLINE
“RAW”:
  All channels with full sampling (1Hz, 1kHz,…. 20kHz,….)
  File list /virgoData/ffl/raw.ffl (to load in dataDisplay, or your own Matlab or Python script )
  (updated every 5-10minutes)
“TREND”:
  Only channels sampled at 1Hz or less
  min, max, mean, rms of each raw channel (computed over 1s)
  File list /virgoData/ffl/trend.ffl (updated every 30minutes)
  BRMS channels: RMS computed over given band, DQ_BRMSMon*, Hrec, several ENV channels
Quick look over long time stretches
Very useful to look for time evolution of noise
and correlate with slow trends

## Slide 26: DATA streams: ONLINE
Use dataDisplay as an Oscilloscope …

## Slide 27
Pictures (hall, benches)
END of part I