SIESTA simulations
of a power-recycled interferometer

---
Outline
SIESTA simulation of a power-recycled ITF:
how the algorithm works
validation / results
another algorithm: ITF dynamics
final considerations

---
SIESTA command OPitf
Outline:
how the algorithm works
validation / results
another algorithm: ITF dynamics
final considerations
SIESTA command OPitf:
FFT simulation of a power-recycled interferometer
computation of stationary fields inside the ITF
solution searched by successive iterations

---
Power-recycled ITF
The same mechanisms used for a simple FP cavity are extended to a power-recycled ITF.
Basically, the ITF is treated as a set of three communicating cavities:
- North arm cavity
- West arm cavity
- central Michelson
Before addressing the algorithms for the power-recycled itf, I will explain/remind how SIESTA works for a simple FP cavity.
The very same mechanisms are applied to the itf.
So, here is what SIESTA does for a FP cavity:
adjust the cavity to resonance
compute the stationary field

---
Power-recycled ITF
inner
cycles
outer
cycle

---
1. Guess fields

---
2. Lock arm cavities
as for a single FP cavity

---
3. Solve arm cavities
as for a single FP cavity
‘fast’ algorithm works fine
(VIR-0658A-10)

---
4a. Lock power recycling

---
4b. Lock dark fringe

---
5. Solve central Michelson
as for a single cavity,
just more beams to take into account
‘fast’ algorithm does not work here (why?)

---
Again and again
Start again!
lock arm cavities
solve arm cavities
lock PR
lock DF
solve central itf
...

---
Outline:
how the algorithm works
validation / results
another algorithm: ITF dynamics
final considerations
Let’s have a look at some results...
unless otherwise stated : grid 717mm, 256 points
cavity adjustment @ every cycle
pixel size = 2.8mm
= 8 × MiniFiz pixel size

---
Virgo+

---
Virgo+ – no defects
3725.8
3 iterations / 53 seconds
losses_N	= 0.02 ppm
losses_W	= 0.02 ppm
recycling_gain	= 77.989
cavity_gain_N	= 95.548
cavity_gain_W	= 95.548
contrast_defect	= 2.4956e-11
38.994
dark fringe
1
77.989
1
38.994
3725.8
77.988
9.8562e-10

---
Virgo+ – real RoC’s
2632.0
no defects, but real RoC’s & no CHRoCC
354 iterations / 75 min
losses_N	= 0.5 ppm
losses_W	= 0.1 ppm
recycling_gain	= 55.888
cavity_gain_N	= 94.199
cavity_gain_W	= 94.189
contrast_defect	= 1.8780e-02
27.944
dark fringe
1
55.888
0.47496
27.943
2632.3
55.362
0.52430

---
Virgo+ – real maps
493.81
mirror maps on ITMs and ETMs,
extended to 330mm
307 iterations / 88 min
losses_N	= 285.45 ppm
losses_W	= 633.72 ppm
recycling_gain	= 10.771
cavity_gain_N	= 93.172
cavity_gain_W	= 91.692
contrast_defect	= 9.2717e-2
5.0727
dark fringe
1
10.771
8.3164e-2
5.2424
501.78
9.8543
0.46069

---
Virgo+ – real maps & CHRoCC 3600m
mirror maps on ITMs and ETMs, extended to 330mm
Added curvature to simulate CHRoCC -> 3600m
360 iterations / 100 min
losses_N	= 256.82 ppm
losses_W	= 630.73 ppm
recycling_gain	= 17.400
cavity_gain_N	= 93.999
cavity_gain_W	= 92.366
contrast_defect	= 3.0903e-02
803.59
8.1933
dark fringe
1
17.400
2.8851e-2
8.4901
817.80
16.429
0.25430

---
Virgo+ – real maps & CHRoCC 3650m
mirror maps on ITMs and ETMs, extended to 330mm
Added curvature to simulate CHRoCC -> 3650m
275 iterations / 84 min
losses_N	= 263.36 ppm
losses_W	= 434.92 ppm
recycling_gain	= 21.821
cavity_gain_N	= 94.021
cavity_gain_W	= 93.277
contrast_defect	= 2.6534e-02
1017.7
10.468
dark fringe
1
21.821
1.0722e-2
10.640
1025.8
20.831
0.27651

---
Advanced Virgo

---
AdV – no defects
11063
3 iterations / 33 seconds
losses_N	= 2e-03 ppm
losses_W	= 2e-03 ppm
recycling_gain	= 77.985
cavity_gain_N	= 283.71
cavity_gain_W	= 283.71
contrast_defect	= 9.0292e-10
38.993
dark fringe
1
77.985
0.99994
38.993
11063
77.985
3.5659e-8

---
What about the sidebands?
Simulation of AdV with increasing losses in the central ITF
(affected to the PRM)
on the average:
CAR: 4 iterations
SB: 6 iterations
CPU time: 4.5 min

---
Outline:
how the algorithm works
validation / results
another algorithm: ITF dynamics
final considerations
OPglobal card:
FFT simulation of a power-recycled interferometer
computation of the temporal evolution of the fields inside the ITF (‘dynamics’)
already presented in VIR-0563A-10, so I will not go into details
slow but reliable method to validate other results!

---
OPglobal
Virgo+ with real mirror maps (extended to 330 mm)
CPU time depends on # clock ticks:
e.g. 10h for 15000 clock ticks

---
Comparison: ‘stationary’ vs ‘dynamic’
Virgo+ with real mirror maps (extended to 330 mm)
Black: ‘stationary’ solution (OPitf)
Red: ‘dynamic’ solution (OPglobal at the end of the simulation)
493.81
493.57
dark fringe:
5.0727
5.0701
10.771
1
10.766
8.3164e-2
5.2424
501.78
9.8543
8.3540e-2
5.2397
501.53
9.8494
0.46069
0.46049
OPitf
OPglobal

---
Outline:
how the algorithm works
validation / results
another algorithm: ITF dynamics
final considerations

---
Several things to do
Incomplete TODO list:
implement signal recycling
‘fast’ algorithm for the central Michelson (should work in principle but it does not... hunt the bug!)
allow the use of transmission maps
implement FFTW instead of the current FFT implementation
implement multithreading (for instance: carrier and sidebands on different threads)
whatever users want...

---
But most of all...
Some personal considerations:
SIESTA-FFT is a half-sleeping project (no pun intended):
1 developer (me) + 1 user (Romain).
I am leaving the collaboration in two weeks;
Romain will finish his PhD ~ october 2012
It is big and heavy and slow to evolve, but I think still useful because:
it tries to be as versatile as possible
it integrates with the Virgo software environment (e.g. input/output in frame format)
it can be easily run in `batch’ mode via shell scripts
the source code is open to everybody in the collaboration
However:
It really needs a boost:
in the dreamworld, 1 developer 100% on SIESTA
even more important: a user community (if nobody uses it, there is no reason to develop)

---
That’s all folks
Thank you.
Nice SIESTA to everybody.

---
SPARES

---
FP cavity
Before addressing the algorithms for the power-recycled ITF, I will explain/remind how SIESTA works for a simple FP cavity.
The very same mechanisms are applied to the ITF.
So, here is what SIESTA does for a FP cavity:
adjust the cavity to resonance
compute the stationary field

---
adjust a FP cavity

---
solve a FP cavity

---
About the use of mirror maps
WARNING #1
Measured maps are about 900×900 pixels wide.
Reducing map resolution is delicate, since it can significantly influence gain and losses.
After some tests, my conclusion is that the best practice is to reduce map resolution by averaging an integer number of neighbor pixels (e.g. averaging over 2×2 pixels, 4×4, etc.).
This is what one gets for Virgo+ West cavity:
no resampling of the maps
(why losses so high?
see next slide)

---
About the use of mirror maps
WARNING #2
Why losses are so high?
→ The maps have a diameter of 312 mm.
If we extend artificially the West map to 330 mm:

---
Power-recycled ITF
SECOND POSSIBILITY:
cavities adjusted only at the beginning
inner
cycles
outer
cycle